## Slide 1: 8051 microcontroller
Introduction
Pin diagram
Architecture

## Slide 2
Memory
ROM
RAM
Main function of processor is to execute a program
Processor
Non Volatile
Volatile
Power off, still data present (permanent)
Eg. Secondary mem (hard disk)
Power off, data lost (temporary)
Eg. Primary mem (RAM chip)
I/O ports
I/O devices
System Bus
To connect processor,
memory and I/O ports
Address
Bus
Data
Bus
Control Bus
Processor based system
All these components are assembled within a single chip.this chip is called as microcontroller including timer
Timer
Programs are fetches from memory

## Slide 3
Memory
ROM
RAM
Processor
Programs
4 KB
Data
128 Bytes
I/O ports
Timer
8 bit
P0
P1
P2
P3
8 bit
2, 16 bit
8051
Serial port
TXD
RXD

## Slide 5
Pin Diagram of 8051
(40 pins)

## Slide 6
Processor
8 bit
INT
ROM
Programs
4 KB
INT
RAM
Data
128 Bytes
XTAL 1
XTAL 2
RESET
ALE
(external access) EA
(Prog status PSEN
enable)
VCC
GND
8 bit
P0.0 … PO.7 / AD0 – AD7
P1.0 … P1.7 / X (no alternative)
P2.0 … P2.7 / A15 – A 8
P3.0 … P3.7 / Alt fun of P3
TXD
RXD
P3.0
P3.1
INT 0
INT 1
P3.2
P3.3
P3.4
P3.5
P3.6
P3.7
Alternative functions of P3
T0
T1
RD
WR
Serial port
External h/w ints
Ex. Playing game and call occurs
Timer CLK i/p
8051 gets clock here
12 MHz
(12 millions per seconds)
EXT
ROM
EXT
RAM
parallel port
Alternate pins

## Slide 7
XTAL 1 & XTAL 2(crystal oscillator pins ): As VCC apply crystal start oscillating i.e. it gives continuous 0 and 1 i.e. clock pulses
RESET : This pin is used to reset the 8051. it only reset RAM not ROM
ALE : 8051 has 16 bit address bus and 8 bit data bus. When ALE = 0 , AD0-AD7 work as data bus and when ALE = 1 this lines work as a address
BACK
Serial port : bit by bit transfer / on bit at a time
example : mic, telephone
Disadv : slower than parallel port
Adv: cheaper, cost less than parallel port
TXD : To transfer data RXD : To receive data
Timer:
There are 2 ,16 bit timers are available in 8051
Timers are used to generate a delay by counting
To count timer requires clock pulses(to triggered)
T0 and T1 are used to give clock pulses to the timer
Oscillator clk is not used for timer because clk freq is 12 mhz which is too fast for timer,which only used to speed up the processor

## Slide 8
P0 to P3 Port :
8051 consist four parallel ports
All ports are bidirectional so they can be used as input or output.
Individual port is 8 bit so we can connect 8 devices to a single port
Hence we can connect total 32 devices by using 8051 port
Example for output port:
8 LEDS are connected to any port so LEDS can be made ON or OFF(light system) from 8 LEDS we want to glow last LED then simply pass 01 H
Musical fountains : LEDS are connected to fountain jets
All the ports are bit addressable (each line of port can be individually made 0 or 1)
example : 8 Fans are connected with 8 lines of any port of 8051, individually
single fan can be on or off without disturbing others.
Instructions used : SETB, CLR
SETB P0.0
CLR P0.0
Example for Input port:
Piano
BACK

## Slide 9
EA : (External Access) :
8051 having internal RAM as well as external RAM
Internal RAM and external RAM both are works separately. Instructions for both are different
In case of external and Internal ROM either use both at a time or any one.
Whether to use internal ROM or not is the choice of programmer.
If we want to use internal ROM then first internal ROM comes and at the end of internal ROM external ROM begins
0000 | 
0FFF | 
Internal ROM
1000 | 
FFFF | 
External ROM
EA = 1
If we want to discard int ROM then only external ROM can be used by making EA=0
0000 | 
Internal ROM
0000 | 
External ROM
EA = 0
BACK

## Slide 10
BACK
Why there are alternate function of port?
Why there is no separate address/data bus?
Answers :
You may not always need address / data bus
Processor and memory both are present inside the 8051
Only for external RAM or ROM address bus and data bus are required

## Slide 11
EXT
ROM
64 KB
EXT
RAM
64 KB
8051
P3.6
P3.7
PSEN
RD
WR
Add line is 16 bit
216 = 26 x 210 = 64 KB
1.There fore ext RAM and ROM individually 64 Kb.
2. Addresses are duplicates for both
3. Control signals are used to differentiate
0000 | 
FFFF | 
0000 | 
FFFF | 
To read data from ext ROM
For Ext RAM : RD , WR s/g are used
For Ext ROM : PSEN s/g is used
BACK
Example :

## Slide 12
CPU
MEMORY
I/O ports, Timer

## Slide 13
8051 reads the data from external RAM at location 4000
8051
0000 | 
4000 | 25
FFFF | 
EXT
ROM
0000 | 
4000 | 36
FFFF | 
EXT
RAM
2. Control signal generated by RD = 0
1. For above example both 4000 location gets selected by address bus
AD = 4000
C = RD
3. Data 25 will read by 8051 through data bus
D = 25
Sequence :

## Slide 14
ALU
8 bit
A
8 bit
B
8 bit
PSW
8 bit
A & B gives operands to
ALU
ALU performs the operations
Result store
into reg A
Status will store
into PSW
1
2
3
4
BACK
Data Registers

## Slide 15
Reg A : (Accumulator) : it is used to hold the first operand as well as result. It will accumulating the result there fore it is called as accumulator
Reg B : it is used with multiplication and division instructions i.e. MUL AB
ALU : A and B gives operand to the ALU, then ALU will perform all arithmetic, logical operations on given operand and result will store into accumulator and status will store into PSW.
PSW : (Program Status WORD) :
PSW contains the status of the result after each operation performed by ALU.
Working of PSW is similar with flag register of processor.
PSW can changed by ALU
In case of 8051 PSW can also modified by programmer(i.e. mov psw, 10h)
BACK
Data Registers

## Slide 16
PC(Program Counter):
PC is used to hold the address of next instruction.
It is always used to hold the address of an instruction
PC is 16 bit register
0000 | 
0001 | 
FFFF | 
Address
Data
PC
PC + 1
PC will autoincrement by 1
Next
Address Registers

## Slide 17
Address
Data
Internal
RAM
Internal
ROM
128 Bytes
4 KB
8 bit
8 bit
16 bit
8 bit
These registers contains data
These registers contains address
Whatever
contents of this line is available
for programmer
BACK

## Slide 18
DPTR (Data Pointer 16 bit):
Data pointer is used to gives the address of data
Data can be accessed by following manner
a. In sequence b. In reverse c. Random
------
------
------
------
------
------
------
------
------
It is not autoincrement
It is control by programmer
Address Registers
DTPR gives the 16 bit address of 8 bit data because 8051 has 16 bit address
To modify DPTR we have to perform 16 bit operation because DPTR is 16 bit
But 8051 works on 8 bit data it means 8051 performs 8 bit operation in one cycle
So to modify DPTR it requires more than one cycle
To avoid above problem two registers are used i.e. DPH and DPL
Example :

## Slide 19
DPH (data pointer higher byte) & DPL (data pointer lower byte) :
1 2 3 4 H L | 
1 2 3 5 H L | 
FFFF | 
Address
Data
DTPR
If DPTR is 1234 and wants to increment by 1
It means actually we want to increment lower byte
So instead of increment whole number only lower byte needs to perform operation
There fore choice is given to programmer to increment lower byte or higher byte individually
DTPR + 1
So programmer can use full DTPR for 16 bit operation or DPH / DPL for 8 bit operation
BACK

## Slide 20
Address
Data
Internal
RAM
Internal
ROM
128 Bytes
4 KB
8 bit
8 bit
16 bit
8 bit
NEXT
A
8 bit
D
8 bit
D - 8 bit
A
16 bit

## Slide 21
00 H | 
01 H | 
02 H | 
. | 
. | 
7F H | 
Address
Data
8 bit
8 bit
Size of the internal RAM is 128 bytes
27 = 128
7 bits are used to generate the address
Internal RAM
0000 0000
0000 0001
…
…
0111 1111
00 H
01 H
…
…
7F H
Internal ROM
Size of the internal ROM is
4 KB
4 KB = 22 x 210
12 bits are used to generate the address
0000 H | 
0001 H | 
0002 H | 
. | 
. | 
0FFF H | 
Address
Data
16 bit
8 bit
0000 0000 0000 0000
0000 0000 0000 0001
…
…
0000 1111 1111 1111
0000 H
0001 H
…
…
0FFF H
Next
BACK

## Slide 22
Before latch red color line is data bus, Data bus only carries data not store
After latch it becomes port , So latch is used to store data

## Slide 23
8051
0000 | 
3000 | 46
FFFF | 
EXT
ROM
0000 | 
3000 | 55
FFFF | 
EXT
RAM
PSEN = 1
RD = 0