## Slide 1: 8051 timer section

## Slide 2
Memory
ROM
RAM
Processor
Programs
4 KB
Data
128 Bytes
I/O ports
Timer
8 bit
P0
P1
P2
P3
8 bit
2, 16 bit
8051
Serial port
TXD
RXD

## Slide 3
Delay
Software delay
Hardware delay
Software delay generated by using NOP instruction.
By putting NOP instruction into the loop delay can be achieved.
But processor again involve for fetching decoding and executing this instruction.
Timer is used to generate hardware delay

## Slide 4
Timer is used to produce a delay
For example : Air Conditioner
We set the off time or on time for AC, for this needs to generate delay of specific time.
If processor is responsible to generate delay it will not able to perform other task like controlling temperature, display temperature on screen and etc.
So to make processor free to perform other important operations timer is used to generate the delay
Once delay over timer will inform to processor to do the related task.

## Slide 5
2 , 16 bit up - counter
To produce two delay simultaneously two timers are used
T0 (16)
T1 (16)
TH0 (8)
TL0 (8)
TH1 (8)
TL1 (8)
1. To generate delay first we need to
load count value.
2. In case of 8051, 16 bit counters are
used.
There fore count value is 16 bit number i.e. 65,535
Range for counter is 0000 to FFFF
To hold count value we required special registers i.e. SFR
But SFR is 8 bit , so we required 2 , 8 bit SFR
2 SFR
2 SFR
4 SFR
There are two types of counter
UP
5
4
3
2
1
0
DOWN
5
4
3
2
1
0
Example count = 0005 H
0 0 0 5 H
H
L
MOV TL0 , # 05H
MOV TH0 , # 00H
Count(16)
0005 H
CLK
FFFF
0006
0007
0008
0000
When counter is incremented after FFFF H it will rollback to the 0000 H and this event is called as Timer Overflow
Timer Overflow
When counting is over timer will send an interrupt to processor through TF tag (TF0 , TF1)
When counting is over timer will send an interrupt to processor by setting TF = 1

## Slide 6
TF :
Timer overflow flag is used indicate the overflow of counter
It is also used to store pending status of interrupts ( INT 0 , INT 1 , serial interrupt)
In 8051 whenever any event occurs which is suppose to be interrupt first of all TF flag become 1
When counting is over timer will send an interrupt to processor by setting TF = 1
INT (TF0 =1)
Program
ISR
TF0 =0
Steps :
Load count
Apply clock pulse
Timer send interrupt
Before load count value we need to calculate count value

## Slide 7
How to calculate count value :
0004
Count(16)
0005 H
1
0005
1
2
0003
2
3
0002
0001
3
4
4
5
5
Counting over means overflow of timer
0000
If down counter :
We required exact 5 clock pulses

## Slide 8
FFFF
0006
0007
0008
0000
Timer Overflow
Count(16)
0005 H
CLK
Count value = FFFF – 5 + 1
= 65535 -5
= 65530 + 1
= 65531 (FFFB H)
Count(16)
0005 H
1
FFFC
FFFB
1
2
FFFD
2
3
FFFE
FFFF
3
4
4
5
5
Counting over means overflow of timer
0000
There fore +1 is used
Formula for count value = Max count – Desired count + 1
Up counter :

## Slide 9
Difference between counter and timer :
Timer and counter are not exact same
They are almost same
Its totally depend upon the intension of programmer whether device is used as a counter or timer
Timer :
0 1 2 3 4 5
Counter :
0 1 2 3 4 5
Space between digits are fixed
Space between digits are not fixed

## Slide 10
A company manufacturing some product.
There is a conveyor belt which is used to pass the product
And packaging department having container to collect the product
The condition is one container should contain only 100 products.
One container should contain 100 products
Product
Company
Conveyor belt
Packaging department
Example :
Somebody needs to count the product
person
programming
(Manual process)
(Mechanical process)
Automation
Counting can be done by Laser Light
Laser light for counting
One container should contain 100 products
Product
Transmitter
Receiver
Photocell : light on gets charged
Company
Packaging department
Conveyor belt
1. Light is continuously falling
2. At the receiver side there is a photo cell.
3. The moment light appear on photo cell it will be in logic 1
state.
4. When product pass it through this light it will cut the rays,
so photo cell will change it’s state from 1 to 0.
5. When product pass away from light again it will become logic 1

## Slide 11
Example 1 :
One container should contain 100 products
Product
Laser light for counting
Transmitter
Receiver
Photocell : light on gets charged
Count(16)
0005 H
CLK
Example 2 : In bank counting notes

## Slide 12
TCON
TIMER Control
TF1
TR1
TF0
TR0
IE1
IT1
IE0
IT0
INTRRUPT
TIMER
1 = Timer overflow
(Auto cleared)
1 = RUN
0 = STOP
(Software Control )
1 = If external interrupt occurs
(Auto cleared)
1 = Edge triggered
0 = Level triggered
First 4 bits of TCON are related with Timer to control the timer
Last 4 bits of TCON are purely related with external interrupt

## Slide 13
These bits are 1 , when timer overflow occurs and auto clear
Both are independent overflow flags, not depend upon each other. Which means one flag can be set and other can be auto clear.
TF0 & TF1 (Timer Overflow Flags) :
BACK
TR0 & TR1 (Timer Run Bits) :
This bits are used to RUN or STOP the timer.
When this bit is 1 then timer should start to run and when 0 then timer should stop.
These bits are software control bits , which means through software, programming or using instruction programmer can start or stop these bits.
Example : SETB TR0
CLR TR1
Timer Bits

## Slide 14
XTAL 1
XTAL 2
8051 gets clock here
12 MHz
(12 millions per seconds)
Divide by 12
T0
T1
External clock
1 Mhz
If frequency is fixed
If frequency is variable
Timer
If internal freq is used which is unchanged
Counter
If external freq is used which is variable

## Slide 15
When interrupt occurs processor will go into the ISR, but in 8051 when interrupt occurs some flag will become 1.
There are two hardware / external interrupt pins i.e. INT0 and INT1 in case of 8051, hence IE0 and IE1 these two separate flags are available.
Whichever interrupt occur these flags become 1 and then processor come to know that interrupt is occur.
As soon as processor will enters into the respective ISR these flags will auto clear.
IE0 & IE1 (Interrupt Enable Flags) :
BACK
Interrupt Bits

## Slide 16
IT0 & IT1 (Interrupt Type Flags) :
BACK
Interrupt Bits
Interrupt
Edge Triggered
Level Triggered
When interrupt occurs on any one of the pin or on both pin (INT0 & INT1) of 8051, the status of these pin will be 1 because these are active high signal
Interrupt recognized on edge is called as edge triggered interrupt
Interrupt recognized on level is called as level triggered interrupt
Example : on mobile screen we want to display M letter multiple time and continuously , so we need to press and release button continuously….it is called edge triggered
Example : on mobile screen we want to display only M constantly, so we need to press button for long time without releasing the button….it is called level triggered
For computer keyboard exact opposite scenario

## Slide 17
TF1
TR1
TF0
TR0
IE1
IT1
IE0
IT0
INTRRUPT
TIMER
0
0
0
0
1
1
1
1
=
69 H
No timer overflow occurs for timer 1 means timer 1 is still counting
Timer 1 is running
Timer overflow occurs for timer 0 means timer 0 is not counting
Timer 0 is stop
TIMER 1
TIMER 0
Interrupt 1
Interrupt 0
It has accured
It is level triggered
It has not accured
It is edge triggered
Example : Programmer has loaded value 69 h in TCON , explain what is happened ?

## Slide 18
TMOD
Gate
C/T
M1
M0
Gate
C / T
M1
M0
XTAL 1
XTAL 2
Divide by 12
T0
T1
1 Mhz
INT0
INT1
T0
T1
Button
To start or
Stop timer
Hardware control for timer no interrupt option
1 = counting is controlled by INTX(INT0 or INT1) (hardware control)
1 = counter
0 = timer
00 | Mode 0
01 | Mode 1
10 | Mode 2
11 | Mode 3
T0
T1
Counter
If using external clk
Timer
If using internal clk
Whenever gate term occurs in electronics which means enable
Timer can run or stop by two methods
Hardware control
By using buttons which can connect to INT pins not timer
Software control
By making TR0 & TR1
0/1
TIMER Mode
0 = counting is independent of INTX its purely (Interrupt) (timer control by software)
Two bits are used to select timer mode
Interrupt through button

## Slide 19: Logic diagram for TMOD
fOX
Divide by 12
Clk to counting stage
1
Internal
External
C
T
C/T
T1 or T0 Pin
1
1
1
TR1 or TR0
Gate
1
1
0
INTX for timer
When both input 1 then only output is 1 , if any i/p 0 then o/p is 0
To transfer clock to counting this line should be enable by passing
Necessary has to 1
Bcz S/W control primary
One i/p is not sufficient
When something 1 then output is 1 , both i/p cannot be o
If o/p of gate is 0 then another i/p has to be 1
1
XTAL 1
XTAL 2
Divide by 12
T0
T1
1 Mhz
INT0
INT1
T0
T1
Button
To start or
Stop timer
H/W control
/ 0
/ 1
or 0
INTx for
Interrupt
If this 0 then counting not take place

## Slide 20: Modes of timer
0 0 | Mode 0
0 1 | Mode 1
1 0 | Mode 2
1 1 | Mode 3
M1
M0
M0 and M1 these two bits of TMOD is responsible to select mode of timer

## Slide 21: 13 bit timer counter
Mode 0
TLx
THx
TFx
Clock
From input stage
05 bits
08 bits
Interrupt
TL0 or TL1 register to store lower byte of count value
TH0 or TH1 register to store higher byte of count value
TF0 or TF1 flag set when overflow occurs and generate interrupt

## Slide 22
How to store bytes :
If number is 35
H
L
3
5
Suppose we want to increment count
3
6
Will always increment lower byte
7
8
9
0
When lower byte overflow it will automatically increment the higher byte
4
For TH and TL
Count value is 1234
TH
TL
12
34
35
36
FF
TL overflows and now HL increments
13
FF
Timer overflows and it will send interrupt
TLx
THx
TFx
Interrupt
34
12
Always remember in diagram of modes TL is first and then TH
If these block interchange, then working of entire circuit goes wrong
00
00

## Slide 23
TLx
THx
TFx
Clock
From input stage
05 bits
08 bits
Interrupt
TL0 or TL1 register to store lower byte of count value
TH0 or TH1 register to store higher byte of count value
TF0 or TF1 flag set when overflow occurs and generate interrupt
1. Count value is loaded into the TL0 and TH0
2. At every clock pulse lower byte increment by 1
3. As soon as lower byte overflows , higher byte will start to increment.
4. As soon as lower byte overflows , higher byte will start to increment.
5. As soon as higher byte overflows , it will set the timer overflow flag and send the interrupt
1
In case of Mode 0 , maximum load count is 1FFF
Size of TLx register is 05 bits which means
213 = 1FFF
It is used to create artificial serial port which will see in serial port section of 8086

## Slide 24
This mode is used to divide frequency the by 32
TLx
THx
TFx
Clock
From input stage
05 bits
08 bits
Interrupt
1
The size of TL is 05 bits i.e.
25 = 32 i.e. 1F
So after 1st 32 clock pulses TLx will overflow and the overflow of TLx will increment the THx.
12
1. 32 clk pulses
1F
00
Overflow
Of TL
34
35
2. 32 clk pulses
12
1F
00
Overflow
Of TL
36
32. 32 clk pulses
00
Overflow
Of Tx

## Slide 25: 16 bit timer counter
Mode 1
TLx
THx
TFx
Clock
From input stage
08 bits
08 bits
Interrupt
TL0 or TL1 register to store lower byte of count value
TH0 or TH1 register to store higher byte of count value
TF0 or TF1 flag set when overflow occurs and generate interrupt
This mode is used to produces maximum delay, there fore it is preferable mode to produce delay.
Max count = 216 = 65535 = FFFF
FF
FF
00
00
1

## Slide 26: 8 bit timer counter with “Reloaded”
Mode 2
TLx
TFx
THx
08 bits
08 bits
Interrupt
Enable reloaded
Clock
From input stage
Reloaded counter means to load the original counter again after counting.
Once the counting over and overflow occurs at that time the original counter reloaded.
If we want fire alarm after 5 minutes
Then will use
Mode 1
If we want fire alarm after every 5 minutes
Then will use
Mode 2
We required two registers one for counting and second for
loading the original count hence mode 2 uses 8 bit counter.
For
Counting
For
Loading

## Slide 27
Example :
TLx
TFx
THx
08 bits
08 bits
Interrupt
Enable reloaded
Clock
From input stage
For
Counting
For
Loading
If count value is 35 then in both reg
TLx & THx 35 is loaded.
35
35
When TLx overflow it will send 1 to TFx and
Buffer which will enable the buffer and original
count loaded again
1
1
1
Once to reach FF instead of 00 it will loaded
with original count i.e. 35
This mode will not stop automatically until and unless program
stop it.

## Slide 28: 2, 8 bit timer using T0
Mode 3
TL0
TF0
Clock
From input stage
08 bits
08 bits
Interrupt
TH0
TF1
Clock
From input stage
08 bits
08 bits
Interrupt
To make 3 timers available
T1 (16)
T0 (16)
TH0 (08)
TL0 (08)
TF1
TF0
16 bit T0 divided into two part to make two individual 8 bit timer.
TL0 of timer 0 uses TF0 flag of timer 0 for overflow
TH0 of timer 0 uses TF1 flag of timer 1 for overflow
Timer 1 can counts but can’t generate overflow because all flags are used.
T1 is used with serial port of 8051 to produce delay while serial communication. So T1 purely dedicated to serial port in that case we have only one timer left. At that time mode 3 is used

## Slide 29: Timer program

## Slide 30
To produce square wave using timer
WAP to generate square wave of 1 KHz on P1.2
Display (CRO)
To generate given Square wave on CRO we have to use following steps
To send 0 on P1.2, instruction is CLR P1.2
To send 1 on P1.2, instruction is SETB P1.2
By using above method following output will generate
Because 8051 do it above operation so fast it will display white screen
We have to generate square wave with equal delay :
0
0
0
0
1
1
1
Delay = 0.5 ms
XTAL 1
XTAL 2
Divide by 12
T0
T1
1 Mhz
T0
T1
P1.2
0 , 1
12 MHz
1 KHz
0.5 ms
0.5 ms
1 ms
Because inverse of 1 KHz is 1 MS

## Slide 31: Steps for timer related programs

## Slide 32
Program :
 | SJMP MAIN | Continue
DELAY: | MOV TMOD , # 01 H | 
 | MOV TL0, # 0C H | 
 | MOV TH0 , # 0FE H | 
 | MOV TCON , # 10 H *MOV TCON.4, #01H *SETB TR0 | 
WAIT: | JNB TF0 , WAIT | 
 | CLR TR0 | 
 | CLR TF0 RET | 
IT IS A STANDARD PROGRAM OF DELAY
STEPS :
SELECT MODE
LOAD COUNT
START TIMER
Gate
C/T
M1
M0
Gate
C/T
M1
M0
T0
T1
0
0
0
1
0
0
0
0
SELECT MODE
2. LOAD COUNT
TF1
TR1
TF0
TR0
IE1
IT1
IE0
IT0
INTRRUPT
TIMER
0
0
0
0
0
0
0
1
3. START TIMER
JNB : JUMP IF NO BIT I.E. JUMP IF TF0 = 0
THIS ISTRUCTION GETS EXECUTE TILL COUNTING IS
OVER
NOT CUMPOLSARY
BUT ALWAYS CLEAR REG
0
0
0
0
1
1
1
Count to be loaded = (FEOC)h
MAIN : | CLR P1.2 | Send 0
.
 | ACALL DELAY | Delay
 | SETB P1.2 | Send 1
 | ACALL DELAY | Delay

## Slide 33
Step 1 : Find out timer clock (Tf) with following formula
** And always convert Tf into KHz by multiplying with 1000 **
12
Tf (Timer clock frequency ) = XTAL frequency (oscillator frequency) in MHz
Possible Oscillator frequency can be asked : (in exam)
1. | 12 MHz
2. | 11.0592 MHz
3. | 22 MHz
If not mentioned then take any 1 of given frequency and calculate
Tf which is in KHz

## Slide 34
1. Calculation of Tf if XTAL = 12 MHz
12
Tf (Timer clock frequency ) = XTAL frequency (oscillator frequency) in MHz
Tf = 12 MHz = 1 MHz = 1 x 1000 = 1000 KHz
12
2. Calculation of Tf if XTAL = 11.0592 MHz
Tf = 11.0592 MHz = 0.9216 MHz = 0.9216 x 1000 = 921.6 KHz
12
3. Calculation of Tf if XTAL = 22 MHz
Tf = 22 MHz = 1.833 MHz = 1.833 x 1000 = 1833.33 KHz
12

## Slide 35
Step 2 : Calculate the time (T) required to produce clock pulse
Convert into microseconds by multiplying with 1000
Tf
T (Time) = 1
1. XTAL = 12 MHz then Tf = 1000 KHz
T = 1 = 0.001 KHz = 0.001 x 1000 = 1 micro sec
1000 KHz
2. XTAL = 11.0592 MHz then Tf = 921.6 KHz
T = 1 = 0.001085 KHz = 0.001085 x 1000 = 1.085 micro sec
921.6 KHz
3. XTAL = 22 MHz then Tf = 1833.33 KHz
T = 1 = 0.0005454 KHz = 0.0005454 x 1000 = 0.545 micro sec
1833.33 KHz

## Slide 36
Step 3 : Find out count or delay (any one is given)
Always convert delay from mili sec to micro seconds by multiplying with 1000
Time (T) in micro sec
Count = Given delay in (mili sec)
a) If delay is given then need to calculate count
b) If count is given then need to calculate delay
Time (T) in micro sec
Delay = Count X
Convert into micro sec dividing by 1000

## Slide 37
Step 4 : Calculate the count to be loaded
Convert decimal count value into hexadecimal value for loading into TH and TL SFRs
count value = Max count – Desired count + 1
Count value = 65535 – Desired count + 1

## Slide 38
Step 5 : Write a program
Load mode of timer into TMOD
Load count value into TH and TL
Make port or port bit 0 or 1
Start timer (either TCON or TRx bits)

## Slide 39: Timer programs

## Slide 40
1. WAP to generate a pulse with the width of 5 mili sec (ms) on P1.3 , Assume XTAL = 11.0592 MHZ , timer 0 is
used with mode 1
5 ms
Solution :
2.5 ms
2.5 ms
ON time
Off time
Delay :
2.5 ms
Step 1 : Find out timer clock (Tf) with following formula
Calculation of Tf if XTAL = 11.0592 MHz
Tf = 11.0592 MHz = 0.9216 MHz = 0.9216 x 1000 = 921.6 KHz
12
Step 2 : Calculate the time (T) required to produce clock pulse
XTAL = 11.0592 MHz then Tf = 921.6 KHz
T = 1 = 0.001085 KHz = 0.001085 x 1000 = 1.085 micro sec
921.6 KHz

## Slide 41
Step 3 : Find out count or delay ( delay is given)
Time (T) in micro sec
Count = Given delay in (mili sec)
Desired Count = (2.5 mili sec x 1000 ) / 1.085 micro sec
= 2500 micro sec / 1.085 micro sec
= 2304.14
= 2304
Always convert delay from mili sec to micro seconds by multiplying with 1000
Consider only integer part
Step 4 : Calculate the count to be loaded
Count value = 65535 – Desired count + 1
= 65535 – 2304 + 1
= 65535 – 2303
= 63232
Decimal
Hex count value = F700
Loaded into TH and TL
Step 5 : Write a program
Load mode of timer into TMOD
Load count value into TH and TL
Make port or port bit 0 or 1
Start timer (either TCON or TRx bits)

## Slide 42
Program :
This program only for 1 pulse
0
1
count value = F700
Gate
C/T
M1
M0
Gate
C/T
M1
M0
T0
T1
0
0
0
1
0
0
0
0
TMOD = 01 h
 | CLR P1.3 | 
 | ACALL DELAY | 
 | SETB P1.3 | 
 | ACALL DELAY | 
DELAY | MOV TMOD , # 01 H | 
 | MOV TL0, # 00 H | 
 | MOV TH0 , # 0F7 H | 
 | SETB TR0 | 
WAIT: | JNB TF0 , WAIT | 
 | CLR TF0 | 
 | CLR TR0 | 
 | RET | 

## Slide 43
1. WAP to generate a square wave of 1KHZ on P1.4 , Assume XTAL = 12 MHZ , timer 0 is
used with mode 1
2. WAP to generate a square wave with on time of 3 mili sec and off time of 10 mili sec on all pins of port 0 ,
Assume XTAL = 22 MHZ , timer 1 is used with mode 1
3. WAP to generate a pulse with the width of 3 mili sec (ms) on P0.4 , Assume XTAL = 11.0592 MHZ , timer 1 is
used with mode 1