## Slide 1: Interrupt of 8051

## Slide 2
Microcontroller
Device 1
Device 2
Device N
service
service
service
A single microcontroller can serve several devices. There are two methods to provide services are :
Polling
Interrupts

## Slide 3
Polling :
In polling microcontroller continuously monitors the status of given device.
When status condition met, it performs the service.
After that it moves on to monitor next device until each one is serviced.
Although polling can monitor the status of several devices and serve each of them as certain conditions are met, it is not an efficient use of microcontroller.
The polling method cannot assign priority since it checks all devices in Round-robin method.
In this method microcontroller can not ignore the service request of device
Interrupt :
In interrupt method, whenever any device needs its service, the device notifies the microcontroller by sending it an interrupt signal
Upon receiving an interrupt signal, the microcontroller interrupts whatever it is doing and serves the device.
Program associated with interrupt is called as ISR (interrupt service routine) .
Advantage of interrupt is that the microcontroller can serve many device as per priority.
In this method microcontroller can ignore the interrupt request of device

## Slide 4
ISR (Interrupt Service Routine :
For every interrupt, there must be an interrupt service routine (ISR), or interrupt handler.
When an interrupt invoked, the microcontroller runs the interrupt service routine.
Program
ISR
RETI
Interrupt

## Slide 5
IVT(Interrupt Vector Table):
For every interrupt there is a fixed location in memory that holds the address of its ISR .
The group of memory locations set aside to hold the addresses of ISRs is called the interrupt vector table.
Sr.No. | Interrupt | ROM Location (Hex) | Pin | Flag Clearing
1. | Reset | 0000 | 9 | Auto
2. | External H/W interrupt 0 (INT 0) | 0003 | P3.2(12) | Auto
3. | Timer 0 interrupt (TF 0) | 000B |  | Auto
4. | External H/W interrupt 1 (INT 1) | 0013 | P3.3(13) | Auto
5. | Timer 1 interrupt (TF 1) | 001B |  | Auto
6. | Serial COM interrupt (RI & TI) | 0023 |  | Programmer clears it

## Slide 6
Steps in Executing Interrupt :
It finishes the current instruction and saves the address of next instruction (PC) on stack.
It also saves the current status of all the interrupts internally (Not on the stack)
It jumps to a fixed location in memory called the interrupt vector table (IVT) that holds the address of the interrupt service routine (ISR).
The microcontroller gets the address of the ISR from the IVT and jumps to it. It starts to execute the ISR until it reaches the last instruction of subroutine i.e. RETI (return from interrupt).
Upon RETI instruction it returns, first controller gets the PC address from stack and then start execution from given address.
Click to add text

## Slide 7
Whenever any event occurs which causes an interrupt something is set (flags).
If two interrupts occurs simultaneously then at a time processor can execute only one interrupt so
another interrupt must be store somewhere therefore whenever interrupt occurs flags are set.
What happened when interrupts occurs simultaneously ? ?
Reset
INT 0
Timer 0
INT 1
Timer 1
Serial Interrupt
0000 H
0003 H
000B H
0013 H
001B H
0023 H
TCON
IE1
IE0
1 = occurred
Auto cleared
TCON
TF1
TF0
1 = occurred
Auto cleared
Ti
Ri
Common ISR
Separate ISR
Separate ISR
SCON
Ti
Ri
1 = occurred
Cleared by programmer
Interrupt
ISR (0023 H)
if (Ti=1)
{
Transmission
}
if (Ri=1)
{
Reception
}
CLR Ti
CLR Ri

## Slide 8
Reset
0000 H
When reset pin is activated, 8051 jumps to address location 0000 H.
Reset is used to Call BIOS which is used to initialize the system.
Size of reset ISR is 3 bytes that is from 0000 H to 0002 H which is not sufficient for BIOS
program because size of BIOS program is depend upon the application .
So LJMP instruction is used to jump the main program or BIOS program.
Size of the LJMP is 3 bytes.
INT 0
0003 H
+ 3
Timer 0
INT 1
Timer 1
Serial
Interrupt
000B H
0013 H
001B H
0023 H
+ 8
+ 8
+ 8
+ 8
Size of all remaining interrupts are 8 bytes.
These 8 bytes contains address of specified ISR
Program
ISR
RETI
Interrupt
Push PC on stack
PC = ISR address
POP PC from stack
CALL ISR
3 bytes
1 bytes
If want to add something before ISR again we can CALL ISR and RET (4 bytes)
Disabled all interrupts
At a time only one
Interrupts are enabled
Return instruction
RET
RETI
Simply return which is used in CALL
Return with re-enable the interrupt

## Slide 9
IE (Interrupt Enable): SFR
There is a register called IE (Interrupt Enable) that is responsible for unmasking or masking the interrupts
EA
X
ET2
ES (serial)
ET1
(Timer 1)
EX1
(INT 1)
ET0
(Timer 0)
EX0
(INT 0)
1 = Enable
0 = Disable
1 = Enable all
0 = Disable all
Reserved for
8052
1
0 1 0 0 0
0
EA = Main switch of Power
ES,ET1,EX1,ET0,EX0 = Fan,light etc
If main switch is ON then only single fan or light can be ON or OFF i.e. EA = 1
If main switch is OFF then even though single fan or light ON it not matters . i.e. EA = 0

## Slide 10
1. WAP that displays a value of ‘Y’ at port 0 and ‘N’ at port 2 and also generate the square wave of 10KHz with
timer 0 in mode 2 at pin P1.2 with XALT = 22 MHz ( using interrupt )
0.1 ms
Solution :
0.05 ms
ON time
Off time
Delay :
0.05 ms
Step 1 : Delay is given in KHz
1 Khz = 1 ms
10 Khz = 0.1 ms
0.05 ms
Step 2 : Find out count or delay ( delay is given)
Time (T) in micro sec
Count = Given delay in (mili sec)
Desired Count = (0.05 mili sec x 1000 ) / 0.545 micro sec
= 50 micro sec / 0.545 micro sec
= 91.74
= 91
Step 4 : Calculate the count to be loaded
Count value = FF – Desired count + 1
= 255 – 91 + 1
= 165 (decimal)
= A5 (hex)
( mode 2 is 8 bit )

## Slide 11
IP (Interrupt Priority): SFR
X
X
PT2
PS (serial)
PT1
(Timer 1)
PX1
(INT 1)
PT0
(Timer 0)
PX0
(INT 0)
1 = High Priority
0 = Low Priority
Reserved for
8052
1 0 0 0 1
If two ES and ET1 occurs simultaneously then ES has highest priority because PS =1.
If ES and EX0 or EPT1 and EX1 occurs at a time which having same priority then such situation is called as clash or Tie
If there is a tie then it follows default priority
5 4 3 2 1
Default Priority
For default priority 1= highest priority
5= lowest priority

## Slide 12
Program :
 | ORG 0000 H | 
 | LJMP Main | 
 | ORG 000B H CPL P1.2 | 
 | RETI ORG 0030 H | 
MAIN | MOV TMOD , # 02 H | 
 | MOV TL0, # 0A5 H | 
 | MOV TH0 , # 0A5 H MOV IE, #82 H | 
 | SETB TR0 | 
BACK: | MOV P0, #’Y’ | 
 | MOV P2, #’N’ | 
 | SJMP : BACK | 
Sr.No. | Interrupt | ROM Location (Hex)
1. | Reset | 0000
2. | External H/W interrupt 0 (INT 0) | 0003
3. | Timer 0 interrupt (TF 0) | 000B
4. | External H/W interrupt 1 (INT 1) | 0013
5. | Timer 1 interrupt (TF 1) | 001B
6. | Serial COM interrupt (RI & TI) | 0023
EA
X
ET2
ES (serial)
ET1
(Timer 1)
EX1
(INT 1)
ET0
(Timer 0)
EX0
(INT 0)
1
1
0
0
0
0
0
0
Skip reset ISR
ISR of Timer 0
ISR program for timer 0
Loan main after last interrupt ISR
Timer related settings
IE settings
Start timer
Port 0 displays Y
Port 2 displays N
While timer is running
When timer overflow occurs TF0 set and interrupt occurs and processor will jump to the Timer 0 ISR i.e. at location 000B H