## Slide 1: Serial Port of 8051

## Slide 2
Communication
The word communication specifies, data transfer between two points.
The data may be digital or analog in nature.
We will consider only digital data transfer because processor is digital circuit.
There are two types of data transfer
- Parallel data transfer(no. of bits at a time) – parallel communication
Faster but costly because required many lines
- Serial data transfer(1 bit at a time) – serial communication
Slower but cheaper because required single line
For long distance mostly serial communication preferred.
Advantage from serial communication : It is cheap
Advantage from parallel communication : Fast
8051 : Cheap + Fast

## Slide 3
Parallel
To
Serial
converter
Serial
To
Parallel
converter
Serial
1 bit data
Parallel 8 bit
data
Parallel 8 bit
data
Serial Data Transfer

## Slide 4: Types of communication system :
Simplex :
The simplex is one way transmission. The connection exists such that data transfer takes place only in one direction. System A is transmitter and B is receiver
Transmitter
Receiver
System A
System B
2. Duplex :
The simplex is two way transmission. There are two groups.
a) Half duplex b) full duplex
a) Half Duplex :
it is a connection between two terminals such that, data may travel in both the directions, but transmission activated at a time.
System A
System B
Transmitter
Transmitter
Receiver
Receiver
OR
System A
System B
Transmitter
Transmitter
Receiver
Receiver
OR / AND
b) Full Duplex :
it is a connection between two terminals such that, data may travel in both the directions simultaneously. So it will contain one way transmission at a time.

## Slide 5: Serial Transmission Formats :
Asynchronous Data Transfer
Synchronous Data Transfer

## Slide 6
Processor
(8)
SBUF(8)
SBUF(8)
RxD
TxD
1 0 1 0 0 1 0 0
0 0 1 0 0 1 0 1
P1 (8)
Require 8 cycles
Require 8 cycles
Require 1 cycle
Processor wants to send/receive data using port, then it will send
8 bit data directly in one cycle using MOV P1, #25H because it it is
8 bit processor, hence it is called parallel data transfer.
Processor wants to send/receive data serially using serial port then
there is only single pin TXD/RXD. Hence processor requires 8 cycles to
transfer/receive 8 bit data. Because 1 bit requires 1 cycle to send or
receive by processor.
If processor involved to send or receive data serially then it will slow
down processor’s speed.
4. To avoid this processor will transfer/receive data through SFRs. There
are two 8 bit SFRs , SBUF
Processor will transfer/receive data into SBUF in one cycle and processor
will be free to perform other operations.
6. SBUF is responsible to transfer /receive data serially
Physically there are two different SBUF reg
which having same name
MOV SUBF , A : Transmitter Buffer
MOV A , SUBF : Receiver Buffer
Introduction of Serial port of 8051

## Slide 7
Memory
ROM
RAM
Processor
Programs
4 KB
Data
128 Bytes
I/O ports
Timer
8 bit
P0
P1
P2
P3
8 bit
2, 16 bit
8051
Serial port
TXD
RXD

## Slide 8
Processor
(8)
0
0
1
0
0
1
0
1
SBUF(8)
TxD
0 0 1 0 0 1 0 1
Before completion of previous data if new data arrives into SBUF then previous data will be loss.
In that situation processor will not check whether the operation is completed or not SBUF will interrupt the processor
IN 8051 whenever an event occur which causes interrupt something is set
1. processor will continuously
check whether SBUF is empty
or not which is time consuming
for processor.
Transmission
Processor wants to send 25 h (0 0 1 0 0 1 0 1) data serially.
2. Processor transfer this data into SBUF using
following instruction : MOV SUBF,A
3. SBUF will transfer bit by bit data using TxD pin.
4. Always LSB goes out first.
5
2
After sending 25 h data serially , processor wants to send another data
for example 69 h
Two methods
2. SBUF will informs to processor
after completion of data
transfer
Transmitter Interrupt Ti =1
Receiver Interrupt Ri =1
Ti =1
RxD

## Slide 9
Processor
(8)
0
0
1
0
0
1
0
1
0
0
1
0
0
1
0
1
SBUF(8)
SBUF(8)
RxD
TxD
1 0 1 0 0 1 0 0
0 0 1 0 0 1 0 1
P1 (8)
Ti= 1
ISR
MOV SBUF , A
CLR Ti
Ti= 1
When complete data has been transmitted Ti become 1
If Ti = 1, processor get the interrupt and it will executes the ISR
Again loads the SBUF with new data
3. Before executing ISR it will clear the Ti flag
4. Ti flag is not auto clear like other flags, it has to be clear by
programmer in ISR.
Transmission

## Slide 10
Processor
(8)
0
0
1
0
0
1
0
1
SBUF(8)
RxD
0 1 0 1 0 0 1 0
Reception
1. SBUF will Receive bit by bit 25 h (0 0 1 0 0 1 0 1) data using RxD pin.
2. Always LSB comes in first.
2
5
Ri =1
3. When complete data has been Received Ri become 1
4. If Ri = 1, processor get the interrupt and it will executes the ISR
Ri= 1
ISR
MOV A , SBUF
CLR Ri
5. Data from SBUF is transfer into the processor
6. Before executing ISR it will clear the Ri flag
7. Ri flag is not auto clear like other flags, it has to be clear by programmer in ISR
SBUF(8)
TxD

## Slide 11
Processor
(8)
0
0
1
0
0
1
0
1
0
0
1
0
0
1
0
1
SBUF(8)
SBUF(8)
RxD
TxD
1 0 1 0 0 1 0 0
0 0 1 0 0 1 0 1
Ri =1
Ti= 1
At the same time data can be send and/or receive
Using two separate pins TxD and RxD
Hence serial communication using 8051 is called as
System A
System B
Transmitter
Transmitter
Receiver
Receiver
OR / AND
it is a connection between two terminals such that, data may travel in both the directions simultaneously. So it will contain one way transmission at a time.
Full Duplex :

## Slide 12: ** Error checking **

## Slide 13
Transmitter
Channel
Receiver
Error occurs on channel
Error Checking performs on
Reception
Where Error Occurs ???
Processor
(8)
0
0
1
0
0
1
0
1
0
0
1
0
0
1
0
1
SBUF(8)
SBUF(8)
RxD
TxD
1 0 1 0 0 1 0 0
0 0 1 0 0 1 0 1
P1 (8)
Error Checking performs after receiving data into SBUF and Before Transferring to processor.
following steps are performed while error checking :
After receiving and before giving to the processor SBUF i.e. serial port will perform error check
If data is valid then it will make Ri = 1 and transfer to the processor
If data is invalid then Ri will remains 0 and data is kept into the SBUF and new data will erased previous invalid data

## Slide 14
Ti (Transmitter Interrupt) :
Ti flag is used in transmission process.
SBUF is used to transfer data serially, when complete data has been transmitted , SBUF will send interrupt to the processor through Ti flag.
Ti = 1 when complete data has been transmitted, otherwise Ti=0
This flag is not auto cleared. Programmer has to cleared this flag at the end of ISR.
Ri (Receiver Interrupt) :
Ri flag is used in reception process.
SBUF is used to receive data serially, when complete data has been received , SBUF will send interrupt to the processor through Ri flag.
Ri = 1 when complete data has been received, otherwise Ri=0
This flag is not auto cleared. Programmer has to cleared this flag at the end of ISR.
BACK

## Slide 15
SM0
SM1
SM2
REN
TB8
RB8
Ti
Ri
SCON
Receiver Enable
00 | Mode 0
01 | Mode 1
10 | Mode 2
11 | Mode 3
Enabled Multiprocessor
Communication in M2,M3
M0 : Not used
M1 : if (SM2 = 1)
{
Ri = 1 (if “stop bit = 1”)
else Ri =0
}
M2,M3 : if (SM2 = 1)
{
Ri = 1 (if “9 th bit = 1”)
else Ri =0
}
d(8)
M0 : Shift register
START
1
0
Always
d(8)
M1 : 8 bit UART
They are
System
generated
Serial port send 0 or 1
STOP
0
d(8)
M2,M3 : 9 bit UART
START
STOP
0/1
1
Programmable bit = 0/1 (by programmer)
Transmission
Reception
9 th bit transmitted
M2,M3
9 th bit receivedM1,M2,M3
1 = complete
0 = Not complete
1 = yes
0 = No
SM2 is a bit by using this programmer can decide to error check or not 0 = no error checking (Ri = 1)
1= error checking (Ri = 0 or 1 )
Structure of mode not working
Error Checking performs on 9 th bit

## Slide 16
SM 2 :
BACK
If SM2 = 0 , do not perform error checking. Ri =1 when complete
data has been transferred and interrupt to processor ,
Ri = 0 at the end of ISR. (SM =0 , Ri =1 or Ri = 0)
Error checking is done at receiver side.
2. During reception we have choice whether we want to
simply accept the data as it is or we have to perform error
checking.
3. By using SM2 bit programmer can decides whether error
checking can be performed or not.
4. If SM2 = 1 , perform error checking. If entered data is valid
then only Ri will become 1 and interrupt given to the
processor. If data is not valid then arrived data will keep
into SBUF only until and unless new valid data has been
arrived. (SM =1, RI=1)
0 1 0 1 0 0 1 0
Ri =1
RxD
Processor
(8)
0
0
1
0
0
1
0
1
SBUF(8)
SBUF(8)
TxD
SM 2 = 1 perform error checking
Data is valid
Data is not valid

## Slide 17
REN (Receiver Enable) :
This bit is used to enabled the reception of 8051 serial port.
BACK
0 1 0 1 0 0 1 0
RxD
Processor
(8)
0
0
1
0
0
1
0
1
SBUF(8)
Reception
Ri =1
SBUF(8)
TxD
If REN =1 , then receiver is enabled and allowing to enter
the data at the receiver side.
Allowed to enter data into SBUF
3. If REN =0 , then receiver is disabled and not allowing to
enter the data at the receiver side.
Not Allowed to enter data into SBUF
NOTE : There is no TEN bit i.e. transmission enabled. Because
if we don’t want to send data then simply don’t
transfer it.

## Slide 18
Example :
0
d(8)
M2,M3 : 9 bit UART
START
STOP
0/1
1
Programmable bit = 0/1 (by programmer)
SM0
SM1
SM2
REN
TB8
RB8
Ti
Ri
Only free channels
Setup Box 1
Setup Box 2
Cable wire to transfer the data (all channels)
to all setup box
T.V.
T.V.
All channels (paid and free)
SM2= 1
SM2= 0
0 = no error checking
1= error checking
When cable distributer wants to send free channels he will distribute channel on wire with 9 th bit = 1
a) for first setup box there is error checking perform and
9 th bit is 1 it means valid data is send
b) for second setup box no error checking so data can be
directly goes to the setup box
no error checking
error checking
Free channels :
Paid channels :
When cable distributer wants to send Paid channels he will distribute channel on wire with 9 th bit = 0
a) for first setup box there is error checking perform and
9 th bit is 0 it means invalid data is send it will not
accept data
b) for second setup box no error checking so data can be
directly goes to the setup box

## Slide 19: Mode explanation :
Transmission
Reception
Calculation of Baud rate (transfer rate)

## Slide 20
Mode 1
8 bit UART
START
1
0
STOP
data
It is 8 bit UART.
There is start bit (0) before data and stop bit (1) at the end of data.
There are total 10 bits in the packet.
Processor sends 8 bit data into SBUF and transmission starts.
Serial port will send 0 as a start bit.
SBUF send bitwise data
Serial port will send 1 as a stop bit.
After complete data has been transferred SUBF will interrupt to processor by making Ti =1
1. Transmission :
Processor
(8)
0
0
1
0
0
1
0
1
0
0
1
0
0
1
0
1
SBUF(8)
SBUF(8)
RxD
TxD
0 0 1 0 0 1 0 1 1
0
1
Ti =1
Ti= 1
ISR
MOV SBUF , A
CLR Ti

## Slide 21
Mode 1
2. Reception :
Processor
(8)
0
0
1
0
0
1
0
1
0
0
1
0
0
1
0
1
SBUF(8)
SBUF(8)
RxD
TxD
0 0 1 0 0 1 0 1 1
0
1
Ti =1
0 0 1 0 0 1 0 1 1
0
1
Serial port first receive 0 as a start bit followed by 8 bit data and at the end 1 as a stop bit (total 10 bits).
But the size of SBUF is 8 bits and received data size is 10 bits
There is no place to store 2 bits, so need to discard 2 bits. i.e. start and stop bit.
If start and stop bits discarded then
what about error checking ???
Error checking is optional
( if SM2 = 0 then no error checking)
start and stop bits are not used for error checking
Before start with use of start and stop bit will see synchronous and asynchronous mode

## Slide 22
1. Sender and receiver both are
operating on common clock.
2. Sender can send data and CLK
Synchronous
Asynchronous
1. Sender and receiver do not
operate on common clock.
2. Sender can send only data not CLK
Both are always at same frequency
Sender
Receiver
Sender wants to send 00 H data. i.e. 00000000 (total 8 0’s)
Sender goes sending 0’s.
In this case can’t say how many 0’s are there. May be 2 0’s , 3 0’s or 1000 0’s
00 H
How to know the number of 0’s
4. If receiver samples this line (read this line) exactly at the
same frequency at which sender is sending.
If sender’s interval = receiver’s interval then only
8- 0’s look like 8- 0’s
6. If sender sends 10 bits / sec and receiver receives data 8 bits / sec
then receiver loss 2 bits.
Sender and receiver always on same frequency
Synchronous : on same frequency and shared common CLK
CLK

## Slide 23
Asynchronous : on same frequency but not shared common CLK
Sender
Receiver
Example :
Sender sends 00 H to the receiver and take break of ½ hour means no communication for ½ hour.
After ½ hour sender again sends 00 H data.
When sender sends first 00 H data , line was ______
For next ½ hour there is no signal pass on therefore line was in the state of last i.e. 0
After ½ hour sender sends next data i.e. again 00 H , therefore the state of line was _______
00 H
½
00 H
Sender :
Receiver :
Both are always at same frequency
Both are working on same frequency receiver knows the sample rate, so receiver samples first 8 bits.
Receiver don’t have idea about the next signals of line whether is next data or garbage value, hence sender will accept the garbage value as a data with sampling.
Hence we required stop bit (1) to inform the receiver that data bits are over.
Now some how receiver understand that garbage value received hence until any changes occurs on line it will not accept next data.
But next data is again 00 H
Receiver will not accept the actual data.
Hence we required start bit (0) to inform the receiver that has to be start
00 H
Stop bit (1)
½
00 H
Start bit (0)
Example 2 :
Sender
Receiver
00 H
½
FF H
Deadline in UART is always 1, for starting of comm required 0 on line

## Slide 24
Mode 1
2. Reception :
Processor
(8)
0
0
1
0
0
1
0
1
0
0
1
0
0
1
0
1
SBUF(8)
SBUF(8)
RxD
TxD
0 0 1 0 0 1 0 1 1
0
1
Ti =1
0 0 1 0 0 1 0 1 1
0
1
Serial port first receive 0 as a start bit followed by 8 bit data and at the end 1 as a stop bit (total 10 bits).
But the size of SBUF is 8 bits and received data size is 10 bits
There is no place to store 2 bits, so need to discard 2 bits. i.e. start and stop bit.
Mode 1 is 8 bit UART, sender and receiver works on same frequency and there is always start (0) and stop (1) bit.
Start bit (0) is discarded and stop bit (1) will be stored into RB 8 flag of SCON
Discarded
Will store into RB 8
SM0
SM1
SM2
REN
TB8
RB8
Ti
Ri

## Slide 25
Baud rate
2
SMOD
32
X
=
T1 overflow
SMOD
PCON
0 / 1
Baud rate
2
0
32
X
=
T1 overflow
1
32
X
=
T1 overflow
2
32
X
=
T1 overflow
Baud rate
2
1
32
X
=
T1 overflow
Processor
(8)
0
0
1
0
0
1
0
1
0
0
1
0
0
1
0
1
SBUF(8)
SBUF(8)
RxD
TxD
0 1 0 1 0 0 1 0 0 1
1 0 0 1 0 0 1 0 1 1 0
P1 (8)
To send each bit T1 generate delay
T1
3. Calculate baud rate:
Mode 1

## Slide 26
Mode 2,3
Processor
(8)
0
0
1
0
0
1
0
1
0
0
1
0
0
1
0
1
SBUF(8)
SBUF(8)
RxD
TxD
data
T1
0
1
9 th bit
1/0
SM0
SM1
SM2
REN
TB8
RB8
Ti
Ri
9 th bit
1/0
data
0
1
9 th bit
1/0
9 th bit
1/0
Baud rate
(M1,M3)
2
SMOD
32
X
=
T1 overflow rate
Baud rate of mode 1 is same as baud rate of mode 3
Baud rate
(M2)
2
SMOD
32
X
=
Fosc/12
Timer 1 is used to produce delay (variable) depend on count value
Divide by 12
Fixed

## Slide 27
d(8)
M0DE 0 :
It is called shift register.
In this mode data is always send using RXD pin at sender side and always receive using RXD pin at receiver side.
One every clock pulse new bit shifted out from sender and on every clock pulse new bit shifted in at receiver.
There fore it is called as shift register.
Baud rate = Fosc / 12.
There is no start and stop bit is used therefore it is fastest than other modes.
Sender
Receiver
TXD
CLK
RXD
(OUT)
RXD
(IN)
0 0 1 0 0 1 0 1
TXD
CLK
Sender
Receiver
00 H
CLK
½
NO
CLK
00 H
CLK
Mode 0 is synchronous mode

## Slide 28
System A
System B
Transmitter
Transmitter
Receiver
Receiver
OR / AND
Transmitter
Receiver
System A
System B
Simplex :
System A
System B
Transmitter
Transmitter
Receiver
Receiver
OR
2. Half Duplex :
3 Full Duplex :
MODE 0
synchronous
MODE 1,MODE 2,MODE 3
asynchronous
RxD
Transmit
Receive
TxD
CLK
Sender is life long either sender or receiver
Sometime sender and sometime receiver
Both simultaneously
011010
RxD
RxD
TxD
TxD
011010

## Slide 29: Serial Port Program
Write a program to transmit data at specified baud rate
Mode 1

## Slide 30
9600
4800
2400
Standard baud rate
Baud rate :
It is a rate at which data is transferred or received in serial communication.
Ask a particular baud rate which means as a programmer we are in a mode where baud rate selected by us.
There are only two modes which are selectable M1 and M3
Because BR (M1,M3) = 2 SMOD / 32 X T1. overflow rate
(variable).
M1 is preferable mode as compare to M3 because in case of M3 there is extra burden on programmer to send 9 th programmable bit.
In case of serial port program, calculation of baud rate is important.
Example : Radio channels
If we want to listen 93.5 we have to set 93.5 channel. If it is change to 93.7 then will get disturbance. There fore frequency or baud rate is important.

## Slide 31
Write a program to transmit 45 H at 9600 baud rate ( Assume MODE 1 )
SBUF
XTAL 1
XTAL 2
Divide by 12
T1
1 Mhz
45 H
0 0 1 0 0 0 1 0 1 1
TxD
INT
Processor send 45 H into SBUF and transmission starts.
SBUF will responsible to send bit-by-bit data through TxD pin along with start and stop bit.
There is a delay between each bit which is produced by Timer 1 (T1).
Internal clock is apply to the T1.
Need to assign count value for T1 , so once counting is over timer 1 will overflow and triggered to SUBF to send the bit.
Delay By T1
Hence timer overflow rate = counting rate = Fosc / 12
Baud rate
2
SMOD
32
X
=
T1 overflow
How to decide count value to overflow the timer and get specified baud rate?????
Overflow rate = data transfer rate

## Slide 32
SBUF
XTAL 1
XTAL 2
Divide by 12
T1
1 Mhz
45 H
TxD
INT
0
1. If count = 3
Serial pot will send 0 as a start bit.
Timer will start the counting using internal clock and count value.
After 3 clock pulses timer will overflow and interrupt to the SBUF to send one bit.
Again on next 3 clock pulse timer will overflow , interrupt to the SBUF and SBUF will send next bit.
1
0
1
0 1 0 0 0
1
2. If count = 5
SBUF
XTAL 1
XTAL 2
Divide by 12
T1
1 Mhz
45 H
TxD
INT
0
1
0
1
0 1 0 0 0
1
After 5 clock pulses timer will overflow and SBUF will send the bit
3. If count = 1
SBUF
XTAL 1
XTAL 2
Divide by 12
T1
1 Mhz
45 H
TxD
INT
0
1
0
1
0 1 0 0 0
1
After every 1 clock pulse timer will overflow and SBUF will send the bit
Which one is faster ???

## Slide 33
Write a program to transmit 45 H at 9600 baud rate
Baud Rate | Count | Count to be loaded
28800 | 1 | FF
14400 | 2 | FE
9600 | 3 | FD
4800 | 5 | FA
2400 | 12 | F4
Mode 1:
Baud rate
2
SMOD
32
X
=
T1 overflow rate
Assume SMOD = 0 which is default
Baud rate
2
0
32
X
=
T1 overflow rate
Overflow rate = Counting Rate
FOS
12
11.0592
MHz
6
12
X 10
T1 used as timer
Counting rate = FOS / 12
For max BR, (fastest baud rate) T1 must do ‘1’ count
Overflow rate = counting rate
1
32
X
=
BR
1
32
X
=
=
28800
In this case Timer (M2) is used because Timer – M2 is auto reload mode.
Count = 8 bit
TL1
TF1
TH1
For loading
For Counting
8 bit
8 bit
To get standard baud rate always take Fosc is 11.0592
By taking other freq will get ans in fraction.
For given program specified baud rate is 9600 and for this baud rate count to be loaded is FD

## Slide 34
Flow Of Program :
Write a main program in which we have to transfer the number into reg i.e. A
Create a subroutine program which is responsible to perform data transfer data serially with all the settings.
This is a standard program to transfer data serially only data which is to be send and baud rate can be changed.
So with the changed data only need to call subroutine in main program.
For subroutine first need to select mode of serial port using SCON reg.
Then select timer mode using TMOD.
load count value and start timer.
Till now actual transfer is not started. Just we have set frequency for timer.
Mov data from accumulator to SBUF for transmission.
Now SBUF sending bit by bit data after every timer overflow.
Wait till all bits transferred
After transmission over stop the timer and clear the Ti flag and resume to the main program.

## Slide 35
Program :
MAIN : | MOV A, # 45 H | 
 | ACALL Transfer | 
Here | SJMP Here | 
Transfer | MOV SCON , # 40 H | 
 | MOV TMOD , # 20 H | 
 | MOV TL1, # 0FD H | 
 | MOV TH1 , # 0FD H | 
 | MOV TCON , # 40 H | 
 | MOV SBUF , A | 
WAIT: | JNB Ti , WAIT | 
 | CLR TR1 | 
 | CLR TF1 | 
 | CLR Ti RET | 
Gate
C/T
M1
M0
Gate
C/T
M1
M0
T0
T1
0
0
0
0
0
0
1
0
TF1
TR1
TF0
TR0
IE1
IT1
IE0
IT0
INTRRUPT
TIMER
0
0
0
0
0
1
0
0
Wait for TI to become 1
LOAD COUNT
SM0
SM1
SM2
REN
TB8
RB8
Ti
Ri
0
0
0
0
0
1
0
0
Clear TR1 (Stop T1)
Clear TF1 (overflow = 0)
Clear Ti (Ti = 0)
Transfer starts